## Slide 1: A5U – Sidepanel Blanking Die Scrap recovery device for BL5 Cassino Cold

## Slide 2
Die Layout – top view
Direction of scrap evacuation
FLOW

## Slide 3
Die Layout – Side view
Chute to evacuate the scrap
FLOW
500 mm
550 mm
290 mm
Transfer height above bolster: 90 mm

## Slide 4
Die Layout – Side view
Transfer height above bolster: 90 mm
FLOW

## Slide 5
Illustration scrap recovery process
Side panel
Conveyor belts
Rotating table
This collage shows a top view of the blanking line and describes the recovery process visually.

## Slide 6
Picture of front of press -> Lifting Gate
A window must be integrated into the lifting gate through which the scrap can be evacuated to the outside.

## Slide 7
Picture of front of press -> inaccessibility with a forklift
As the area is inaccessible for forklifts during production time the scrap recovery device must be craneable.

## Slide 8
Picture of the inside of the press -> scrap chute
It is likely that the scrap chute (yellow) must be modified as the transfer height of the scrap is only 90 mm above the bolster.

## Slide 9
Picture of the inside of the press -> Lightbarrier
Currently the lightbarriers are always active as the press can be operated with open lifting gate
There a 2 separate safety circuits, one secured by the lifting gate and one secured by the diagonal lightbarriers
Modification of safety controls required
(incl. Risk assessments, CE)

## Slide 10
Scrap recovery device (Mulhouse)

## Slide 11
Blank pallet with blank guide (Sochaux or Mulhouse)